## Slide 1: The TPM Guide
Total Productive Maintenance

## Slide 2: 1. TPM definition (1)
A company-wide team-based effort to build quality into equipment and to improve overall equipment effectiveness
Total
  all employees are involved
  it aims to eliminate all accidents, defects and breakdowns
Productive
  actions are performed while production goes on
  troubles for production are minimized
Maintenance
  keep in good condition
  repair, clean, lubricate

## Slide 3: 1. TPM definition (2)
TPM combines the traditionally American practice of preventive maintenance with Total Quality Control and Total Employee Involvement, to create a culture where operators develop ownership of their equipment, and become full partners with Maintenance, Engineering and Management to assure equipment operates properly everyday.

## Slide 4: 2. Origins of TPM
Dr. Deming introduced statistical analysis and used the resulting data to control quality during manufacturing (TQM)
Some general concepts of TQM did not work well in the maintenance environment
The need to go further than preventive maintenance was quickly recognized by those companies who were committed to TQM
Maintenance became an integral part of TQM in the early 90’s

## Slide 5: 3. TPM principles
Increase Overall Equipment Effectiveness (OEE)
Improve existing planned maintenance systems
The operator is the best condition monitor
Provide training to upgrade operations and maintenance skills
Involve everyone and utilize cross-functional teamwork

## Slide 6: 4. Eight major pillars of TPM
Autonomous Maintenance
Planned Maintenance
Equipment and process improvement
Early management of new equipment
Process quality management
TPM in the office
Education and training
Safety and environmental management

## Slide 7: 4. Eight major pillars of TPM 4.1. Autonomous Maintenance (1)
Train the operators to close the gap between them and the maintenance staff, making it easier for both to work as one team
Change the equipment so the operator can identify any abnormal conditions and measure deterioration before it affects the process or leads to a failure

## Slide 8: 4. Eight major pillars of TPM 4.1. Autonomous Maintenance (2)
7 steps are implemented to progressively increase operators knowledge, participation and responsibility for their equipment
  1. Perform initial cleaning and inspection
  2. Countermeasures for the causes and effects of dirt and dust
  3. Establish cleaning and lubrication standards
  4. Conduct general inspection training
  5. Carry out equipment inspection checks
  6. Workplace management and control
  7. Continuous improvement

## Slide 9: 4. Eight major pillars of TPM 4.2. Equipment and process improvement
Objective: maximize efficiency by eliminating waste and manufacturing losses
Manufacturing losses are categorized into 13 big losses:
  Equipment losses (6)
  Manpower losses (4)
  Material losses (3)

## Slide 10: 4. Eight major pillars of TPM 4.2. Equipment and process improvement 4.2.1. Equipment losses
Downtime
loss
Speed loss
Quality loss
Equipment failure / breakdowns
Set-up / adjustments
Minor stopping / idling
Reduced speed
Process errors
Rework / scrap

## Slide 11: 4. Eight major pillars of TPM 4.2. Equipment and process improvement 4.2.2. Manpower and material losses
Manpower
losses
Material
losses
Cleaning and checking
Waiting instructions
Waiting quality confirmation
Material yield
Energy losses
Waiting materials
Consumable material losses

## Slide 12: 4. Eight major pillars of TPM 4.2. Equipment and process improvement 4.2.3 Overall Equipment Effectiveness (OEE)
OEE figures are determined by combining the availability and performance of your equipment with the quality of parts made
OEE measures the efficiency of the machine during its planned loading time. Planned downtime does not effect the OEE figure.

## Slide 13: 4. Eight major pillars of TPM 4.2. Equipment and process improvement 4.2.3 Overall Equipment Effectiveness (OEE)
Overall Equipment Effectiveness = Availability x Performance x Quality Yield
Availability
Downtime loss
Speed loss
Performance
Quality Yield
Quality loss

## Slide 14: 4. Eight major pillars of TPM 4.2. Equipment and process improvement 4.2.3 Overall Equipment Effectiveness (OEE)
Overall Equipment Effectiveness = Availability x Performance x Quality Yield
Availability = time available for production - downtime
time available for production
Performance = ideal cycle time x number of parts produced
operating time
Quality Yield = total number of parts produced - defect number
total number of parts produced

## Slide 15: 4. Eight major pillars of TPM 4.3. Planned maintenance
Objective: establish Preventative and Predictive Maintenance systems for equipment and tooling
Natural life cycle of individual machine elements must be achieved
    Correct operation
    Correct set-up
    Cleaning
    Lubrication
    Retightening
    Feedback and repair of minor defects
    Quality spare parts

## Slide 16: 4. Eight major pillars of TPM 4.4. Early Management of new equipment
Objective: establish systems to shorten
  new product or equipment development
  start-up, commissioning and stabilization time for quality and efficiency
New equipment needs to be:
  easy to operate
  easy to clean
  easy to maintain and reliable
  have quick set-up times
  operate at the lowest life cycle cost

## Slide 17: 4. Eight major pillars of TPM 4.5. Process Quality Management
Definition: a process for controlling the condition of equipment components that affect variability in product quality
Objective: to set and maintain conditions to accomplish zero defects
Quality rate has a direct correlation with
  material conditions
  equipment precision
  production methods
  process parameters

## Slide 18: 4. Eight major pillars of TPM 4.6. TPM in administrative and support departments
Administrative and support departments can be seen as process plants whose principal tasks are to collect, process, and distribute information
Process analysis should be applied to streamline information flow

## Slide 19: 4. Eight major pillars of TPM 4.7. Education and training
TPM is a continuous learning process.
2 major components
  soft skills training: how to work as teams, diversity training and communication skills
  technical training: upgrading problem-solving and equipment- related skills

## Slide 20: 4. Eight major pillars of TPM 4.8. Safety and environmental management
Assuring safety and preventing adverse environmental impacts are important priorities in any TPM effort

## Slide 21: 5. TPM implementation 3 requirements for fundamental improvement
Increasing motivation: changing peoples attitudes
Increasing competency and peoples skills
Improving the work environment, so that it supports the establishment of a program for implementing TPM

## Slide 22: 5. TPM Implementation 12 steps
Preparation
Kick-off
Implementation
Announcement to introduce TPM
Introductory education campaign for the workforce
TPM Promotion (special committees)
Establish basic TPM policies and goals
Preparation and Formulation of a master plan
Develop an equipment management program
Develop a planned maintenance program
Develop an autonomous maintenance program
Increase skills of production and maintenance personnel
Perfect TPM implementation and raise TPM levels
Stabilization
Develop early equipment management program
Invite customers, affiliated companies and subcontractors

## Slide 23: 5. TPM Implementation 5.1. Announce top management’s decision to introduce TPM
State TPM objectives in a company newsletter
Place articles on TPM in the company newspaper

## Slide 24: 5. TPM Implementation 5.2. Introductory education campaign
Seminars for managers
Slide presentations for all employees

## Slide 25: 5. TPM Implementation 5.3. TPM Promotion
Special committees at every level to promote TPM
Newsletters
Articles
Videos
Posters

## Slide 26: 5. TPM Implementation 5.4. Establish basic TPM policies and goals
Analyze existing conditions
Set goals
Predict results

## Slide 27: 5. TPM Implementation 5.5. Preparation and Formulation of a master plan
A master plan lays out your goals, what you will do to achieve them and when you will achieve them
Detailed plans for each pillar have to be prepared

## Slide 28: 5. TPM Implementation 5.6. TPM kick-off
The main kick-off to TPM should take the form of a formal presentation with all the employees attending
This opportunity can be used to gain the full support of the employees
Invite external customers, affiliated and subcontracting companies

## Slide 29: 5. TPM Implementation 5.7. Develop an equipment management program (1)
The tools of Total Quality Management and Continuous Improvement are applied to the management and improvement of equipment
Form project teams
Select model equipment
  identify equipment problems
  analyze equipment problems
  develop solutions and proposals for improvement

## Slide 30: 5. TPM Implementation 5.7. Develop an equipment management program (2)
Typical membership of a team
  five to seven operators
  a maintenance person
  a technical expert
Tools
  Pareto
  Cause & effect
  Root cause
  Methods Analysis

## Slide 31: 5. TPM Implementation 5.8. Develop a planned maintenance program
Set up plans and schedules to carry out work on equipment before it breaks down, in order to extend the life of the equipment
Include periodic and predictive maintenance
Include management of spare parts and tools

## Slide 32: 5. TPM Implementation 5.8. Develop a autonomous maintenance program
A handing-over of maintenance tasks from specialized maintenance personnel to production operators
Promote the seven steps
Tasks to hand over
  cleaning
  lubricating
  inspecting
  set-up and adjustment

## Slide 33: 5. TPM Implementation 5.10. Increase skills of production and maintenance personnel
The training sessions must be planned shortly after the kick-off presentation.
2 major components
  soft skills training
  technical training
Train leaders together
Have leaders share information with group members

## Slide 34: 5. TPM Implementation 5.11. Develop early equipment management program(1)
The principle of designing for maintenance prevention can be applied to new products, and to new and existing machines.
New products must be designed so that they can be easily produced on new or existing machines
New machines must be designed for easier operations, changeover and maintenance

## Slide 35: 5. TPM Implementation 5.11. Develop early equipment management program(2)
Existing machines:
  analyze historical records for
    trends of types of failures
    frequency of component failures
    root causes of failures
  determine how to eliminate the problem and reduce maintenance through an equipment design change or by changing the process

## Slide 36: 5. TPM Implementation 5.12. Perfect TPM implementation and raise TPM levels
Evaluate for the PM Award: The Japanese Institute for Productive Maintenance runs the annual PM Excellence Award. They provide a checklist for companies applying for the award.
Set higher goals

## Slide 37: 6. TPM Benefits
Increased equipment productivity
Reduced equipment downtime
Increased plant capacity
Lower maintenance and production costs
Approaching zero equipment-caused defects
Enhanced job satisfaction
Increased Return On Investment

## Slide 38: The TPM Guide
Total Productive Maintenance